## Slide 1: Ward: Implementing Arbitrary Hierarchical Policies using Packet Resubmit in Programmable Switches
Mojtaba Malekpourshahraki
Brent Stephens
Balajee Vamanan

## Slide 2: Modern datacenter
Datacenters host multiple applications with different requirements
  Memcache
  Spark
  Backup and replication
Datacenters host multiple competing tenants
  Private datacenters
    Facebook  Product and applications groups
  Public datacenters
    Microsoft Azure  Users renting virtual machines
Multiple tenants and diverse applications per tenant cause contention problem

## Slide 3: Multi-tenancy problems
Fairness
  Large flows may saturate the whole bandwidth
    Long delay for short flows
Pricing and SLA
  Better service for more money
Datacenter needs to isolate the traffic based on a predefined policy
How to handle these problems?

## Slide 4: How to enforce desirable policies
Enforce policies using:
  Congestion control algorithms
    Use congestion signals to change the source sending rate
  Schedulers
    Change the dequeue to enforce desirable policy

## Slide 5: Approaches with policy considerations
Two types of approaches
  End-host based (end-to-end)
  Switch based
UPS
EyeQ
AFQ
Trinity
pHost
Utopia
Sincronia
Silo
pFabric
PIAS
Slytherin
PIFO
At end-hosts
In switches
Fastpass
PIEO
2013
2014
2015
2016
2018
2017
2019

## Slide 6: End-host based approaches
End-host
  Has many queues  only at the end host doesn’t need our requirement
Shortcomings
  Waste of resource
    pHost (Sending RTS)
    Silo (Limiting burst size)
  High computational overhead
    Fastpass (Centralized)
In switch approaches perform faster than end-to-end schedulers
EyeQ
Trinity
pHost
Utopia
Sincronia
Silo
At end-hosts
Fastpass
2013
2014
2015
2016
2018
2017
2019
Notes: Hard to implement
  Utopia (Flow classifier)

## Slide 7: PIFO [SIGCOMM, 2016]/PIEO [SIGCOMM, 2019]
PIFO/PIEO:
  Can implement complex hierarchical programmable scheduling policies
PIFO/PIEO resources on a switch are limited (less than 100 queues)
  Cannot have all possible scheduler
  The number of required queues increases with the number of traffic class
UPS
AFQ
pFabric
PIAS
Slytherin
PIFO
In switches
PIEO
2013
2014
2015
2016
2018
2017
2019

## Slide 8: Key question!
Ward
Can we implement any arbitrary hierarchical policy with limited switch resources in programmable switches?

## Slide 9: Ward - Policy abstraction
Different types of flows, applications, and tenants
  Represent with hierarchical policy
  Directed acyclic graph (DAG)
Tenant 1
Tenant 2
Equal share for tenants
Strict priority for Memcashed over backup traffic
WFQ
Tenant 1
Tenant 2
Pri

## Slide 10: Ward framework
Ward uses control boxes
  One control box for each level of the tree
  First box process the root of the tree
Egress
Parser
Egress
Parser
Queues
Control box 1
Pri
WFQ
Flow 2
Flow 3
Flow 1
Tenant 2
Tenant 1
Control box 1
Control box 2
Control box 2

## Slide 11: Ward framework
Each control box has three steps:
  Counter update
  Comparison engine
  Policy enforcement
Counter
Update
Comparison
Engine
Policy Enforcement
Egress
Parser
Egress
Parser
Queues
Control box 1
Pri
WFQ
Flow 2
Flow 3
Flow 1
Tenant 2
Tenant 1
Control box 1
Control box 2

## Slide 12: Ward framework – Counter update
Dual counter
  Use a single counter to compare two streams of packets (e.g., flow, tenants)
Pri
WFQ
Pri
Flow4
Flow5
Flow6
Flow1
Flow2
Flow3
Three dual counters
C1
C2
C3
C1
C2
C3
C4
C5
C6
Pri
WFQ
Pri
Flow4
Flow5
Flow6
Flow1
Flow2
Flow3
Six counters
  One counter per flow
  One counter per policy node
Counter
Update
Comparison
Engine
Policy Enforcement

## Slide 13: Ward framework – Counter update
-3000
0 B
Dual Update counter:
  Packet from left  increase the counter by a packet size unit
  Packet from right  decrease the counter by a packet size unit
Dual Counter 1
Switch
1500 B
0 B
-1500
Pri
Flow1
Flow2
Flow3
Increase the
dual counter
Decrease the
dual counter
Counter
Update
Comparison
Engine
Policy Enforcement
Packet size: 1500 bit

## Slide 14: Ward framework – Comparison engine
Check the value of the corresponding dual center
  Check if the traffic violates the current policy or not
    If yes: use a rate control policy
Policy node
Flow1
Flow2
Flow3
Counter
If (packet class is in left leaf and counter < 0):
  Choose a policy and add it as meta-data
If (packet class is in right leaf and counter > 0):
  Choose a policy and add it as meta-data
Otherwise
  Bypass the packet
Counter
Update
Comparison
Engine
Policy Enforcement

## Slide 15: Ward framework – Policy enforcement
Merge the result of the previous rate control decisions with the current one
  Enforce the strongest rate control
  Order of rate control decisions
  Drop > Enqueue > ECN mark
Counter
Update
Comparison
Engine
Policy Enforcement

## Slide 16: Example
Two level of policy
  Incoming packet belongs to Flow 2
  Flow 2 has lower priority than Flow 3
Egress
Parser
Counter
Update
Comparison
Engine
Policy Enforcement
Counter
Update
Comparison
Engine
Policy Enforcement
Egress
Parser
NA
Comparison
Engine
Policy Enforcement
 | Policy | Counter | Comparison | Enforce
First Box | WFQ | Update | ECN | 
Second Box | Pri | NA | Drop | 
 | Policy | Counter | Comparison | Enforce
First Box | WFQ | Update | ECN | 
Second Box | Pri | NA | Drop | 
Enough stages
Using resubmit
Pri
WFQ
Flow 2
Flow 3
Flow 1
Tenant 2
Tenant 1

## Slide 17: Example
Egress
Parser
Counter
Update
Comparison
Engine
Policy Enforcement
Using resubmit
Counter
Update
Comparison
Engine
Policy Enforcement
Egress
Parser
NA
Comparison
Engine
Policy Enforcement
Enough stages
 | Policy | Counter | Comparison | Enforce
First Box | WFQ | Update | ECN | 
Second Box | Pri | NA | Drop | 
 | Policy | Counter | Comparison | Enforce
First Box | WFQ | Update | ECN | 
Second Box | Pri | NA | Drop | 
Pri
WFQ
Flow 2
Flow 3
Flow 1
Tenant 2
Tenant 1
Two level of policy
  Incoming packet belongs to Flow 2
  Flow 2 has lower priority than Flow 3

## Slide 18: Evaluation
Evaluation goals
  Can Ward enforces a hierarchical policy in the network?
Measured parameters
  Jain’s index fairness
  99 percentile tail flow completion time
Evaluate Ward in both Mini-net/BMv2 and ns3
  Leaf-spine topology
  All links are 10 Gbps
Tenant 2
Tenant 1
Pri
WFQ
Flow 2
Flow 3
Flow 1

## Slide 19: Fairness BMv2
Ward provides fairness with only 6% lower index compared to the ideal fair queuing

## Slide 20: 90th percentile for short flows
Ward can enforce strict priority compared to FIFO

## Slide 21: Conclusion
We proposed Ward
  Implementing hierarchical policies
  Use packet resubmit in programmable switches if needed
We observed that Ward
  Ward can enforce two-level policy
Future work:
  Implement Ward on programmable switches
  Study the balance of performance loss and the depth of the policy tree
  Optimize Ward architecture to reduce the number of required stages

## Slide 22
Thanks for the attention
Mojtaba Malekpourshahraki
Email: mmalek3@uic.edu
Website: cs.uic.edu/~mmalekpo

## Slide 23
Reserved Slides