## Slide 1
Brent Stephens
Aditya Akella, Mike Swift
NSDI 2019
Loom: Flexible and Efficient NIC Packet Scheduling
Notes: In this talk, we will be continuing on from our previous talk with more scheduling.
This work comes from a design philosophy that any time there are competing accesses contending for a shared resource, we need scheduling
In this case, packets from competing applications are contending for the network inside the NIC, so I am here to argue that we need flexible and efficient packet scheduling inside the NIC

## Slide 2: Loom is a new Network Interface Card (NIC) design that offloads all per-flow scheduling decisions out of the OS and into the NIC
Why is packet scheduling important?
What is wrong with current NICs?
Why should all packet scheduling be offloaded to the NIC?

## Slide 3: Why is packet scheduling important?

## Slide 4: Collocation (Application and Tenant) is Important for Infrastructure Efficiency
Tenant 1
Tenant 2
CPU Isolation Policy:
Tenant 1:
Memcached: 3 cores
Spark: 1 core
Tenant 2:
Spark: 4 cores

## Slide 5: Network Performance Goals
Different applications have differing network performance goals
Low Latency
High Throughput
Notes: Start off with existing hiearchy. Then bring in DAG nodes to show more power -- explain what you want, then bring in nodes and show how they help.
Description of shaping vs ordering too complicated. Perhaps start with a simple example with two endpoints and one node.
So: build this up from simple mem/spark by adding new pieces
This should be 4-5 slides, not one

## Slide 6: Network Policies
Wire
Network operators must specify and enforce a network isolation policy
Enforcing a network isolation policy requires scheduling
Fair_1
Pri_1
VM1
VM2
VM1
Pseudocode
Tenant_1.Memcached -> Pri_1:high
Tenant_1.Spark -> Pri_1:low
Pri_1 -> RL_WAN(Dst == WAN: 15Gbps)
Pri_1 -> RL_None(Dst != WAN: No Limit)
RL_WAN -> FIFO_1; RL_None -> FIFO_1
FIFO_1-> Fair_1:w1
Tenants_2.Spark -> Fair_1:w1
Fair_1 -> Wire
FIFO_1
RL_WAN
RL_None
Notes: Start off with existing hiearchy. Then bring in DAG nodes to show more power -- explain what you want, then bring in nodes and show how they help.
Description of shaping vs ordering too complicated. Perhaps start with a simple example with two endpoints and one node.
So: build this up from simple mem/spark by adding new pieces
This should be 4-5 slides, not one

## Slide 7: What is wrong with current NICs?

## Slide 8: Single Queue Packet Scheduling Limitations
Single core throughput is limited (although high with Eiffel)
  Especially with very small packets
  Energy-efficient architectures may prioritize scalability over single-core performance
Software scheduling consumes CPU
Core-to-core communication increases latency
CPU
NIC
Wire
App 1
App 2
NIC
SQ struggles to drive line-rate

## Slide 9: Multi Queue NIC Background and Limitations
Multi-queue NICs enable parallelism
  Throughput can be scaled across many tens of cores
Multi-queue NICs have packet scheduler that chose which queue to send packets from
The one-queue-per-core multi-queue model (MQ) attempts to enforces the policy at every core independently
  This is the best possible without inter-core coordination, but it is not effective
CPU
NIC
Wire
App 1
App 2
NIC
MQ struggles to enforce policies!

## Slide 10: MQ Scheduler Problems
CPU
NIC (Network Interface Card)
Time (t)
Naïve NIC packet scheduling prevents colocation!
It leads to:
High latency
Unfair and variable throughput
Packet Scheduler

## Slide 11: Why should all packet scheduling be offloaded to the NIC?

## Slide 12: Where to divide labor between the OS and NIC?
CPU
NIC
Option 1: Single Queue (SQ)
Enforce entire policy in software
Low Tput/High CPU Utilization
Option 2: Multi Queue (MQ)
Every core independently enforces policy on local traffic
Cannot ensure polices are enforced
Option 3: Loom
Every flow uses its own queue
All policy enforcement is offloaded to the NIC
Precise policy + low CPU
Wire
Fair_1
Pri_1
VM1
VM2
VM1
FIFO_1
RL_WAN
RL_None
Notes: Start off with existing hiearchy. Then bring in DAG nodes to show more power -- explain what you want, then bring in nodes and show how they help.
Description of shaping vs ordering too complicated. Perhaps start with a simple example with two endpoints and one node.
So: build this up from simple mem/spark by adding new pieces
This should be 4-5 slides, not one

## Slide 13
Loom is a new NIC design that moves all per-flow scheduling decisions out of the OS and into the NIC
Loom uses a queue per flow and offloads all packet scheduling to the NIC

## Slide 14: Core Problem:
It is not currently possible to offload all packet scheduling because NIC packet schedulers are inflexible and configuring them is inefficient
NIC packet schedulers are currently standing in the way of performance isolation!

## Slide 15: Outline
Intro: Loom is a new NIC design that moves all per-flow scheduling decisions out of the OS and into the NIC
Contributions:
Specification: A new network policy abstraction: restricted directed acyclic graphs (DAGs)
Enforcement: A new programmable packet scheduling hierarchy designed for NICs
Updating: A new expressive and efficient OS/NIC interface
Implementation and Evaluation: BESS prototype and CloudLab

## Slide 16: Outline
Contributions:
  Specification: A new network policy abstraction: restricted directed acyclic graphs (DAGs)
  Enforcement: A new programmable packet scheduling hierarchy designed for NICs
  Updating: A new expressive and efficient OS/NIC interface

## Slide 17: What scheduling polices are needed for performance isolation? How should policies be specified?

## Slide 18: Solution: Loom Policy DAG
Two types of nodes:
Wire
Fair_1
Pri_1
VM1
VM2
VM1
FIFO_1
RL_WAN
RL_None
Scheduling nodes: Work-conserving policies for sharing the local link bandwidth
Shaping nodes: Rate-limiting policies for sharing the network core (WAN and DCN)
Programmability: Every node is programmable with a custom enqueue and dequeue function
Loom can express policies that cannot be expressed with either Linux Traffic Control (Qdisc) or with Domino (PIFO)!
Important systems like BwE (sharing the WAN) and EyeQ (sharing the DCN) require Loom’s policy DAG!

## Slide 19: Types of Loom Scheduling Policies:
Scheduling:
All of the flows from competing Spark jobs J1 and J2 in VM1 fairly share network bandwidth
Shaping:
All of the flows from VM1 to VM2 are rate limited to 50Gbps
Because Scheduling and Shaping polices may aggregate flows differently, they cannot be expressed as a tree!
Group by source
Group by destination
Notes: TODO: Link to a bunch of paper titles to motivate the need for shaping

## Slide 20: Loom: Policy Abstraction
Policies are expressed as restricted acyclic graphs (DAGs)
DAG restriction: Scheduling nodes form a tree when the shaping nodes are removed
(b) And (d) are prevented because they allow parents to reorder packets that were already ordered by a child node.
Notes: Start off with existing hiearchy. Then bring in DAG nodes to show more power -- explain what you want, then bring in nodes and show how they help.
Description of shaping vs ordering too complicated. Perhaps start with a simple example with two endpoints and one node.
So: build this up from simple mem/spark by adding new pieces
This should be 4-5 slides, not one

## Slide 21: Outline
Contributions:
  Specification: A new network policy abstraction: restricted directed acyclic graphs (DAGs)
  Enforcement: A new programmable packet scheduling hierarchy designed for NICs
  Updating: A new expressive and efficient OS/NIC interface

## Slide 22: How do we build a NIC that can enforce Loom’s new DAG abstraction?

## Slide 23: Loom Enforcement Challenge
No existing hardware scheduler can efficiently enforce Loom Policy DAGs
Scheduling
Domino PIFO Block
1 x
Shaping
1 x
Scheduling
New PIFO Block?
1 x
Shaping
N x
Requiring separate shaping queues for every shaping traffic class would be prohibitive!

## Slide 24: Insight: All shaping can be done with a single queue because all shaping can use wall clock time as a rank

## Slide 25: Loom Enforcement
In Loom, scheduling and shaping queues are separate
All traffic is first only placed in scheduling queues
If a packet is dequeued before its shaping time, it is placed in a global shaping queue
After shaping, the packet is placed back in scheduling queues
F1
F2
F3
Pri
Mem – 25Gbps RL
Mem – No RL
Spark – No RL
Scheduling
Shaping
F1
F1
F1
F2
F3

## Slide 26: Outline
Contributions:
  Specification: A new network policy abstraction: restricted directed acyclic graphs (DAGs)
  Enforcement: A new programmable packet scheduling hierarchy designed for NICs
  Updating: A new expressive and efficient OS/NIC interface

## Slide 27: PCIe Limitations:
NIC doorbell and update limitations:1
Loom Goal: Less than 1Mops @ 100Gbps
NIC
PCIe
Engine
App
Core
DB1
DB2
DB3
DB4
…
DB_F
PCIe
1
2
1
Latency Limitations:
120-900ns
2
Throughput Limitations:
~3Mops (Intel XL710 40Gbps)
1

## Slide 28: Loom Efficient Interface Challenges
Insufficient data:
Before reading any packet data (headers), the NIC must schedule DMA reads for a queue
Too many PCIe writes:
In the worst case (every packet is from a new flow), the OS must generate 2 PCIe writes per-packet
2 writes per 1500B packet at 100Gbps = 16.6 Mops!

## Slide 29: Loom Design
Loom introduces a new efficient OS/NIC interface that reduces the number of PCIe writes through batched updates and inline metadata

## Slide 30: Batched Doorbells
Using on-NIC Doorbell FIFOs allows for updates to different queues (flows) to be batched
NIC
Per-core
Doorbell
FIFO
App
Core
PCIe
Per-core FIFOs still enable parallelism

## Slide 31: Inline Metadata
NIC
Scheduling metadata (traffic class and scheduling updates) is inlined to reduce PCIe writes
Descriptor inlining allows for scheduling before reading packet data
Wire
DMA Engine
PIFOs
Mem
Q5
Q_F
…
Q1
Q2
Q3

## Slide 32: Outline
Contributions:
  A new network policy abstraction: restricted directed acyclic graphs (DAGs)
  A new programmable packet scheduling hierarchy designed for NICs
  A new expressive and efficient OS/NIC interface
Evaluation:
  Implementation and Evaluation: BESS prototype and CloudLab

## Slide 33: Loom Implementation
Software prototype of Loom in Linux on the Berkeley Extensible Software Switch (BESS)1
http://github.com/bestephe/loom
C++ PIFO2 implementation is used for scheduling
10Gbps and 40Gbps CloudLab evaluation
1
2
Notes: This holds even if every flow is new and if the scheduler is updated

## Slide 34: Loom Evaluation
Can Loom drive line rate? Can Loom enforce network policies?
Experiment: Microbenchmarks with iPerf
Can Loom isolate real applications?
Experiment: CloudLab experiments with memcached and Spark
How effective is Loom’s efficient OS/NIC interface?
Experiment: Analysis of PCIe writes in Linux (QPF) versus Loom
Notes: This holds even if every flow is new and if the scheduler is updated

## Slide 35: Loom 40Gbps Evaluation
Setup:
Every 2s a new tenant starts or stops
Each tenant i starts 4i flows (4-256 total flows)
Fair
T2
T1
T3
T4
Policy: All tenants should receive an equal share.
Loom can drive line-rate and isolate competing tenants and flows
SQ
MQ
Loom
35
Notes: All data center applications are distributed. Network performance is a key aspect of overall application performance.
Take the text out if I’m going to say it
Reduce density of lines

## Slide 36: Application Performance: Fairness
vs
Bandwidth
Hungry
Bandwidth
Hungry
Policy: Bandwidth is fairly shared between Spark jobs
Fair
Loom can ensure competing jobs share bandwidth even if they have different numbers of flows
Linux
Loom
Notes: * Take out dotted lines. Smooth the data some more. Start the data at 0.

## Slide 37: Application Performance: Latency
vs
Latency Sensitive
Bandwidth Hungry
Setup: Linux software packet scheduling (Qdisc) is configured to prioritize memcached traffic over Spark traffic
Pri
MQ cannot isolate latency-sensitive applications!
Chart: 90th Percentile Latency (us)
| Loom | Linux (MQ)
90th Percentile Latency | 1196
90th Percentile Latency2 | 3646
Notes: All data center applications are distributed. Network performance is a key aspect of overall application performance.
Take the text out if I’m going to say it
Reduce density of lines

## Slide 38: Loom Interface Evaluation
Line-rate | Existing approaches: PCIe Writes per second | Loom: PCIe Writes per second
10 Gbps | 833K | 19K
40 Gbps | 3.3M | 76K
100 Gbps | 8.3M | 191K
Worse case scenario:
Packets are sent in 64KB batches and each packet is from a different flow
Loom Goal: Less than 1Mops @ 100Gbps
Notes: This holds even if every flow is new and if the scheduler is updated

## Slide 39: Conclusion
Loom is a new NIC design that completely offloads all packet scheduling to the NIC with low CPU overhead
Loom’s benefits translate into reductions in latency, increases in throughput, and improvements in fairness
Current NICs cannot ensure that competing applications are isolated
Notes: Add a slide (or perhaps say on the next slide) "My work addresses this at X layers of the network. Within a host, ..." Want a good preview, concise statement of what you have done

## Slide 40: Related Work (Eiffel)
Eiffel
NIC Scheduling does not eliminate the need for software scheduling
Loom and Eiffel can be used together
Bucketed priority queues could be used to build efficient PIFOs